## Slide 1
1
Verilog Tips
ECE 554
Department of Electrical and Computer Engineering
Based in part on slides by Andy Phelps, Mikko Lipasti, and Joshua San Miguel
Notes: Begin Lecture:
Welcome class, today we’ll be going over some… general advice for testing and implementing your course projects.

## Slide 2
10/27/2021
2
Outline
Verilog basics
  Simulation vs. hardware description
  Structural vs. behavioral
Module design
  Interfaces, functional specification
  Expected behavior, testbench design
Control path vs data path
Version control
Combinational vs sequential logic
  Maintain separation

## Slide 3: Two Roles of HDL
#1: Specifying digital logic
  Specify the logic that appears in final design
  Either
    Translated automatically (called synthesis) or
    Optimized manually (automatically checked for equivalence)
#2: Simulating and testing a design
  High-speed simulation is crucial for large designs
  Many HDL interpreters optimized for speed
  Testbench: code to test design, but not part of final design
Notes: Okay, so let’s first review what an HDL is. An HDL is of course, a hardware description language which is supposed to describe or specify a digital circuit. Hoffman probably drilled into your head that it is very different from a software programming language like C or Python.
And that’s very true because when we write HDL, one of the main goals we have is to describe some digital circuit which will eventually get synthesized and subsequently taped out into real silicon. As a result we have to think about what the Verilog we write will look like when it is converted into sets of gates. The main way to convince yourself something is synthesizable is to think about the Verilog you have written and see if its functionality can be replicated using a bunch of flops, muxes, gates, and other ece352 primitives.
An HDL also often has extra support facilities that are available for doing design test and simulation, so we often write testbenches with it. In ways, writing HDL for testbenches can be somewhat like writing in a software programming language as we usually don’t synthesize testbenches. However, the parallel nature of hardware and also the simulator is still there so we have to watch out for race conditions.

## Slide 4: Synthesis vs Simulation
HDLs have features for both synthesis and simulation
  E.g., simulation-only operations for error messages, reading files
  Obviously, these can be simulated, but not synthesized into circuits
  Also has constructs such as for-loops, while-loops, etc.
Typically, complex behavioral features most useful in testbenches
  Often do not synthesize, do not belong in design, or use very carefully
    E.g. initial, #, for, while (loop iteration count must be known at synthesis time)
Keep clear distinction between hardware (DUT or design under test) and testbench used for simulation
  Clear/clean module interfaces, behavioral spec
  Employ consistent convention (e.g. mymodule.sv always has mymodule_tb.sv)
Notes: Because HDLs are used for both synthesis and simulation, there is often a wide set of language support provided for simulation which has no corollary in hardware.
Some of these features include $display, initial blocks, dynamically bounded loops where number of iterations is not fixed, and readmemh.
When you are writing HDL for hardware it’s usually best to stay towards dataflow assign and structural connections for the easiest synthesis. Always blocks are pretty handy especially when inferring sequential logic but you have to be very careful when using them to get the desired result.
And another word of advice is to make sure you have your testbench modules named clearly with an _tb suffix so you don’t accidentally add it to the synthesis filelist. It should be clear what is actually part of the design and what is just test code.

## Slide 5: Structural vs Behavioral
Structural constructs specify actual hardware structures
  Low-level, direct correspondence to hardware
    Primitive gates (e.g., and, or, not)
    Hierarchical structures via modules
  Analogous to programming software in assembly
Behavioral constructs specify an operation on bits
  High-level, more abstract
    Specified via equations, e.g., out = (a & b) | c
Not all behavioral constructs are synthesizable
  But even some combinational logic won’t synthesize well
  out = a % b // modulo operation – what does this synthesize to?
Notes: We generally can divide up Verilog into two types: structural and behavioral. Nitpickers will point out that technically there is a third- dataflow for direct gate inference but for our purposes here, we will just consider it a subset of behavioral.
Structural Verilog is the tedious Verilog where you write out everything into gate primitives and nets, port connections. It really is mostly a text form of a 352 circuit.
There is a logical correspondence between each gate, net, and synthesized out equivalent.
Behavorial however moreso describes the function of the circuit and and what it is supposed to do. Missing in the behavorial description is the “how” though because it doesn’t really specify the gates to use. As a result behavior is often the source of synthesis danger. For example it’s not clear how this modulo operator will synthesize. Even operators like division might be a little suspect. Will you get a multicycle divider? What if you want a floating point divider?

## Slide 6: Verilog Structural vs Behavioral Example
  module mux2to1(
  input S, A, B,
  output Out );
  wire S_, AnS_, BnS;
  not (S_, S);
  and (AnS_, A, S_);
  and (BnS, B, S);
  or (Out, AnS_, BnS);
  endmodule
S
Out
B
A
  module mux2to1(
  input S, A, B,
  output Out );
  assign Out = (~S & A) | (S & B);
  endmodule
Behavioral
Structural
Better:
assign Out = S? B:A;
Notes: Do an analysis of the code above.
Point out net list like layout of structural
Dataflow (and behavioral) infers gates

## Slide 7: Structural vs. Behavioral Tips
Behavioral
  Much easier to read, understand, maintain
  Succinct, clear
  Synthesis tool has more freedom to map to best hardware
  Low-level modules should be mostly behavioral
Structural
  Really just a netlist with a specific syntax
  Used primarily in higher-level modules to wire up modules
  Meaningful signal names are key to maintaining readable code
Notes: So how do we suggest you use these types of Verilog? Well generally we use behavorial to write most of our module code, often dataflow for combinational and always for sequential or also combinational, and use structural for connecting each individual module.
Structural, while hard to mess up for synthesis is still not suitable for high speed development.

## Slide 8: Module Design
Module scope
  Module boundaries should correspond to functional boundaries
  Use block diagrams during early design phase
  Should be able to give module a comprehensible name
  Behavioral specification: information hiding
    What does the module do without describing how?
Module size
  If Verilog code spans much more than a “screen” in your favorite HDL editor, it is probably too big
  Refactor into more manageable modules
  Simple, small modules are easier to test
Notes: Okay, on to module design. Generally we encourage you to perform what we call “encapsulation” which means keeping all the internal state inside the module related to its internal workings private or invisible to other modules in the hierarchy. You should not be performing module cross-references across synthesized modules! Although it won’t botch up the synthesis it can be a nightmare if you have to make bug fixes within the module being referenced, or maybe perform logic simplifications… maybe even last minutes ones.
Modules should only interface with other modules through the port list given some behavorial specification of what each port means.
Also important to note, it’s certainly worth breaking up gigantic Verilog modules into smaller modules as they will be easier to test and its easier to reuse smaller modules in other consuming modules than larger monolithic modules.

## Slide 9: Module Interface
Signals:
  Understandable and meaningful names
  Clear semantics
    Delineate control from data
  Pick a naming convention, stick to it, e.g. CamelCase, left_operand, active_low_signal_has_trailing_n
Succinct description of interface operation/semantics
  “As simple as possible but no simpler” (Albert Einstein)
Port count creep
  Usually a symptom of poor module boundaries or poor logic/implementation choices
Notes: Now when defining your interfaces, you should try to attach semantics or meaning to them. Make sure they give a clear indication to their purpose, maybe suffix with _n if active low, etc. Make sure to stick with a consistent naming convention to so you don’t confuse each other when connecting things together. Try to use underscores or camel case but not both (unless there is a semantic difference in your code between them).
Also, you should generally avoid interfaces with large amount of ports in them. Some modules like toplevels are inevitably going to have a lot of ports, but try to keep it minimal as possible. Having many ports is usually a sign that more modularization can be done.
Also having extensive wiring can make routing more difficult either for your physical design team or your synthesizer so it’s best to avoid unnecessary wires.

## Slide 10: Unit Testing
Each module should have a testbench
  Testbenches can use SystemVerilog, $display, file I/O
  Again: consistent naming convention helps
Self-checking testbenches are great
Think carefully about coverage
  Directed random testing is often only feasible path
Notes: Alright now let’s discuss some testing. Specifically, unit testing and regression testing.
A unit test is really a test for an isolated individual module. They are valuable so that the integrator working at the level above can just assume that the underlying module is working.
Your unit tests would ideally cover all the individual permutations of the port list for the best coverage and test the output against some known good result to see if it is correct. Often times a module has way too many bits too actually exhaust every single combination though so we can generally randomize fields that have large bitwidths like addresses and data, while control signals such as write enables, are exhausted in more depth.

## Slide 11: Regression Testing
Testbenches survive throughout design cycle
  Use for regression testing
  Whenever module changes, it should still pass all former unit tests
  May need to add new corner case checks, etc.
Large designs: automated regression tests
  Batch job exercises every testbench, automatically compares results to known good baseline
  Usually a combination of SystemVerilog and scripting language (perl, python, bash)
Often a bug “fix” introduces or exposes a different bug
  Regression testing will help catch these
Notes: Now generally after we’ve developed a bunch of unit tests and also integration tests, we generally re-run them when the code it tests is modified in order to make sure they are still passing the old tests. This is known as regression testing.
Often times regression tests are collected into a large test-suite that gets run automatically before code merges into the master. This is how it was done at AMD and in GDAL an open source C++ project I worked on, and how it is done in most hardware / software development workflows.
As bugs are found, we also add more tests directed at those affected edge cases and then those new tests become part of the suite.

## Slide 12: Data path vs. Control path
If design includes data path (usually arithmetic or logical), separate the data path from the control path
  Into a separate module, unless very straightforward
  Forces you to think about interface (what are your control signals?)
Separate control path (usually FSM)
  Think about your state FFs (regs) just as you did in 352
  Design next-state logic
  Design output logic (these are control signals to data path)
  Mealy vs. Moore vs. Mixed
FSM next state and output logic usually coded using always_comb block with case statement
Notes: Okay so when it comes to your data and control path, the main crux is to separate them clearly in your code as different modules. Data and control have very different semantics when written and data path elements can often be reused independently of the control.

## Slide 13: Version Control
Absolute necessity
  Especially with shared lab computers
Create project on github
Check code in frequently
Enables sanity checks
  Diff against prior versions
  When did something break?
Include all testbenches
Automated or semi-automated (i.e. be disciplined) regression testing is not required, but you won’t regret it.

## Slide 14: Team Coding Standards
Consensus-based, based on recommendations provided here (but up to you to decide)
Enumerate in your microarchitecture report
  The more detail the better
Enforce them during weekly code reviews
  Conducted in triples to reduce probability of interpersonal issues causing conflict
  team lead + team member 1 review team member 2, then flip

## Slide 15: Combinational vs Sequential
Remember, this is real hardware, keep sequential elements and combinational elements distinct
  Sequential: edge-triggered FFs, registers, Block RAMs (<=)
  Combinational: everything else (=)
Rely on always_ff, always_comb, respectively
Notes: Finally, let’s discuss a little bit more on the difference between inferring combinational and sequential logic in behavorial. In general separation of combinational and sequential logic is key to having a successful synthesis.
In System Verilog we have always_ff and always_comb. When inferring flops use always_ff and when inferring combinationals use always_comb. Using the classic always is of course possible but somewhat discouraged since ff and comb provide additional hinting to the design compiler.

## Slide 16: Combinational vs Sequential
And now, it’s your turn!
Time to review (or learn) a bit more on what is synthesizable SystemVerilog.
Notes: Alright, so now we are going to play a game here, where I ask you what if anything is wrong with the following code blocks perhaps helping you avoid some of the most common Verilog synthesis issues.

## Slide 17: Combinational vs Sequential
What’s wrong here?
input a, b;
wire z;
reg ctr;
always@* begin
z = a && b;
if(z) begin
ctr <= ctr + 1;
end
end

## Slide 18: Combinational vs Sequential
What’s wrong here?
input a, b;
wire z;
reg ctr;
always@* begin
z = a && b;
if(z) begin
ctr <= ctr + 1;
end
end
Non blocking in continuous always? Not sure if seq. or comb…

## Slide 19: Combinational vs Sequential
What’s wrong here?
input a, b;
wire z;
logic ctr;
always@* begin
z = a && b;
if(z) begin
ctr = ctr + 1;
end
end

## Slide 20: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] z;
reg [3:0] ctr;
always_ff @(posedge clk, negedge a) begin
if(!a)
ctr <= 4’b0;
ctr += z;
end

## Slide 21: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] z;
reg [3:0] ctr;
always_ff @(posedge clk, negedge a) begin
if(!a)
ctr <= 4’b0;
ctr += z;
end
Uh oh… hanging if… (no else!) Might infer latch

## Slide 22: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] z;
reg [3:0] ctr;
always_ff @(posedge clk, negedge a) begin
if(!a)
ctr <= 4’b0;
else
ctr += z;
end

## Slide 23: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] z;
reg [3:0] ctr;
always_ff @(posedge clk, negedge a) begin
if(!a)
ctr <= 4’b0;
else
ctr += z;
end
+= is BLOCKING!
Not sure if gate or ff inferred.
Also same with ++ / -- operators.

## Slide 24: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] z;
reg [3:0] ctr;
always_ff @(posedge clk, negedge a) begin
if(!a)
ctr <= 4’b0;
else
ctr <= ctr + z;
end

## Slide 25: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] x, z, n;
logic [3:0] ctr;
logic [3:0] acc;
always_ff @(posedge clk, negedge a) begin
if(!a) begin
ctr <= 0;
acc <= 0;
end
else
ctr <= (x + z) - n; acc <= ctr + acc;
end
end

## Slide 26: Combinational vs Sequential
What’s wrong here?
input a, b, clk;
input [3:0] x, z, n;
logic [3:0] ctr;
logic [3:0] acc;
always_ff @(posedge clk, negedge a) begin
if(!a) begin
ctr <= 0;
acc <= 0;
end
else begin
ctr <= (x + z) - n; acc <= ctr + acc;
end
end
Nothing, everything fine and dandy!

## Slide 27: Combinational vs Sequential
What’s wrong here?
input a, b, nxtstate;
logic c;
output v;
always_comb begin
if(nxtstate == 1’b0) begin
c = 1;
end
// This is right because I said so.
// Who can mess up this simple gate?
v = a | b | c;
end

## Slide 28: Combinational vs Sequential
What’s wrong here?
input a, b, nxtstate;
logic c;
output v;
always_comb begin
if(nxtstate == 1’b0) begin
c = 1;
end
// This is right because I said so.
// Who can mess up this simple gate?
v = a | b | c;
end
What if nxtstate is High? Malformed gate inferrence…

## Slide 29: Combinational vs Sequential
What’s wrong here?
input a, b, nxtstate;
logic c;
output v;
always_comb begin
c = 0;
if(nxtstate == 1’b0) begin
c = 1;
end
// This is right because I said so.
// Who can mess up this simple gate?
v = a | b | c;
end

## Slide 30: Combinational vs Sequential
What’s wrong here?
input a, b;
input [3:0] howmany;
output [3:0] z;
integer [3:0] i;
always_comb begin
for(i = 0; i < howmany; i++) begin
z++;
end
end

## Slide 31: Combinational vs Sequential
What’s wrong here?
input a, b;
input [3:0] howmany;
output [3:0] z;
integer [3:0] i;
always_comb begin
for(i = 0; i < howmany; i++) begin
z++;
end
end
Dynamically bounded for loop, of course!

## Slide 32: Combinational vs Sequential
What’s wrong here?
input a, b;
input [3:0] howmany;
output [3:0] z;
integer [3:0] i;
localparam BOUND = 7;
always_comb begin
for(i = 0; i < BOUND; i++) begin
z++;
end
end

## Slide 33: Sequential block
Keep it simple! Suggested coding standards:
Always use always_ff
Have a single sequential block for each module
  All registers, FFs initialized, assigned in one place
  Unless you wish to separate data path from control path (but better to have separate modules for each)
Don’t forget proper reset! (no red lines in simulation)
Include only FF/reg assignment:
  if (reset) my_reg <= 0; else my_reg <= my_reg_next;
Leave all other logic, decisions, if/then/else to combinational logic

## Slide 34: Combinational blocks
Use assign whenever it makes sense
  Most of the data path can usually be built this way
For case statements, use always_comb
Have a single always_comb per module
  Or one for control and one for data
At the top of your always_comb, assign default values to every signal that is assigned in the cases
  Good discipline: add control signal, always add it to top first with sensible default value
  Avoids latches being inferred or forgetting to set signal to a sensible value

## Slide 35: Combinational blocks
Within always_comb, lhs of values that are registered (in FFs) should use a consistent naming convention
  e.g. quotient_next = …
  This helps separate them from control outputs (just wires)
The always_ff block then assigns these at posedge clk:
  quotient <= quotient_next;
I repeat myself: keep sequential and combinational operations distinct in your HDL
  This helps you keep them distinct in your mind as well
  Avoids confusion, strange simulation behavior

## Slide 36: Use SystemVerilog Features
Further reading:
  “Synthesizing SystemVerilog: Busting the Myth that SystemVerilog is only for Verification,” Sutherland & Mills, SNUG-SV 2013
  Slides: https://sutherland-hdl.com/papers/2013-SNUG-SV_Synthesizable-SystemVerilog_presentation.pdf
  Paper (much more): https://sutherland-hdl.com/papers/2013-SNUG-SV_Synthesizable-SystemVerilog_paper.pdf
Notes: If you want to learn a bit more about writing synthesizable SystemVerilog… actually a lot more about it, you can go read this paper here by Stuart Sutherland which is pretty in-depth.
And now, we will discuss the CLASS system.

## Slide 37
10/27/2021
37
Summary
Verilog basics
  Simulation vs. hardware description
  Structural vs. behavioral
Modular design
  Interfaces, functional specification
  Expected behavior, testbench design
Control path vs data path
Combinational vs sequential logic
  Maintain separation
Version control
Coding standards
Systemverilog features